Transparent Standby for Low-Power,
Resource-Constrained Embedded Systems
A Programming Language-Based Approach
Francisco Sant'Anna
francisco@ime.uerj.br
@_fsantanna
www.ceu-lang.org

---
page2 (1)
Our Research Goals

---
page2 (2)
Our Research Goals
Address energy efficiency through rigorous use of standby.

---
page2 (3)
Our Research Goals
1. Address energy efficiency through rigorous use of standby.
2. Target constrained embedded architectures that form the IoT.

---
page2 (4)
Our Research Goals
1. Address energy efficiency through rigorous use of standby.
2. Target constrained embedded architectures that form the IoT.
3. Provide standby mechanisms at the programming language level that scale to all applications.

---
page2 (5)
Our Research Goals
1. Address energy efficiency through rigorous use of standby.
2. Target constrained embedded architectures that form the IoT.
3. Provide standby mechanisms at the programming language level that scale to all applications.
4. Support transparent/non-intrusive standby mechanisms that reduce barriers of adoption.

---
page3 (1)
General Approach
(standby, constrained, programming language, transparent)

---
page3 (2)
General Approach
(standby, constrained, programming language, transparent)
Enforce idle states of execution

---
page3 (3)
General Approach
(standby, constrained, programming language, transparent)
- Enforce idle states of execution
- Infer deepest sleeping mode

---
page3 (4)
General Approach
(standby, constrained, programming language, transparent)
- Enforce idle states of execution
- Infer deepest sleeping mode
- Put device to sleep

---
page3 (5)
General Approach
(standby, constrained, programming language, transparent)
- Enforce idle states of execution
- Infer deepest sleeping mode
- Put device to sleep
- Only awake from interrupts

---
page4 (1)
A Motivating Example

---
page4 (2)
A Motivating Example
Every second, read sensor value and broadcast it.

---
page4 (3)
A Motivating Example
Every second, read sensor value and broadcast it.
Arduino

---
page4 (4)
A Motivating Example
Every second, read sensor value and broadcast it.
Arduino
 while (1) {
   delay(1000);
   int v = analogRead();
   radioWrite(v);
 }

---
page4 (5)
A Motivating Example
Every second, read sensor value and broadcast it.
Arduino
Céu
 while (1) {
   delay(1000);
   int v = analogRead();
   radioWrite(v);
 }

---
page4 (6)
A Motivating Example
Every second, read sensor value and broadcast it.
Arduino
Céu
 while (1) {
   delay(1000);
   int v = analogRead();
   radioWrite(v);
 }
 loop do
   await 1s;
   int v = await AnalogRead();
   await RadioWrite(v);
 end

---
page4 (7)
A Motivating Example
Every second, read sensor value and broadcast it.
Arduino
Céu
 while (1) {
   delay(1000);
   int v = analogRead();
   radioWrite(v);
 }
 loop do
   await 1s;
   int v = await AnalogRead();
   await RadioWrite(v);
 end

---
page4 (8)
A Motivating Example
Every second, read sensor value and broadcast it.
Arduino
Céu
 while (1) {
   delay(1000);
   int v = analogRead();
   radioWrite(v);
 }
 loop do
   await 1s;
   int v = await AnalogRead();
   await RadioWrite(v);
 end

---
page5 (1)
Let’s add concurrency...
Every second, read sensor value and broadcast it.

---
page5 (2)
Let’s add concurrency...
Every second, read sensor value and broadcast it.
Arduino
 while (1) {
   delay(1000);
   int v = analogRead();
   radioWrite(v);
 }

---
page5 (3)
Let’s add concurrency...
Every second, read sensor value and broadcast it.
Stop immediately as soon as a message arrives.
Arduino
 while (1) {
   delay(1000);
   int v = analogRead();
   radioWrite(v);
 }

---
page5 (4)
Let’s add concurrency...
Every second, read sensor value and broadcast it.
Stop immediately as soon as a message arrives.
Arduino
 while (1) {
   delay(1000);
   int v = analogRead();
   radioWrite(v);
 }

---
page5 (5)
Let’s add concurrency...
Every second, read sensor value and broadcast it.
Stop immediately as soon as a message arrives.
Arduino
 while (1) {
   delay(1000);
   int v = analogRead();
   radioWrite(v);
 }

---
page5 (6)
Let’s add concurrency...
Every second, read sensor value and broadcast it.
Stop immediately as soon as a message arrives.
Arduino
 uint32_t lst = millis();
 while (1) {
   if (radioAvail())
     break;
   uint32_t cur = millis();
   if (cur > lst+1000) {
     lst = cur;
     int v = analogRead();
     radioWrite(v);
   }
 }
 while (1) {
   delay(1000);
   int v = analogRead();
   radioWrite(v);
 }

---
page5 (7)
Let’s add concurrency...
Every second, read sensor value and broadcast it.
Stop immediately as soon as a message arrives.
Arduino
 uint32_t lst = millis();
 while (1) {
   if (radioAvail())
     break;
   uint32_t cur = millis();
   if (cur > lst+1000) {
     lst = cur;
     int v = analogRead();
     radioWrite(v);
   }
 }
 while (1) {
   delay(1000);
   int v = analogRead();
   radioWrite(v);
 }

---
page5 (8)
Let’s add concurrency...
Every second, read sensor value and broadcast it.
Stop immediately as soon as a message arrives.
Arduino
 uint32_t lst = millis();
 while (1) {
   if (radioAvail())
     break;
   uint32_t cur = millis();
   if (cur > lst+1000) {
     lst = cur;
     int v = analogRead();
     radioWrite(v);
   }
 }
 while (1) {
   delay(1000);
   int v = analogRead();
   radioWrite(v);
 }

---
page5 (9)
Let’s add concurrency...
Every second, read sensor value and broadcast it.
Stop immediately as soon as a message arrives.
Arduino
 uint32_t lst = millis();
 while (1) {
   if (radioAvail())
     break;
   uint32_t cur = millis();
   if (cur > lst+1000) {
     lst = cur;
     int v = analogRead();
     radioWrite(v);
   }
 }
 while (1) {
   delay(1000);
   int v = analogRead();
   radioWrite(v);
 }

---
page5 (10)
Let’s add concurrency...
Every second, read sensor value and broadcast it.
Stop immediately as soon as a message arrives.
Arduino
 uint32_t lst = millis();
 while (1) {
   if (radioAvail())
     break;
   uint32_t cur = millis();
   if (cur > lst+1000) {
     lst = cur;
     int v = analogRead();
     radioWrite(v);
   }
 }
 while (1) {
   delay(1000);
   int v = analogRead();
   radioWrite(v);
 }

---
page6 (1)
Let’s add concurrency...
Every second, read sensor value and broadcast it.
Stop immediately as soon as a message arrives.
Arduino
 uint32_t lst = millis();
 while (1) {
   if (radioAvail())
     break;
   uint32_t cur = millis();
   if (cur > lst+1000) {
     lst = cur;
     int v = analogRead();
     radioWrite(v);
   }
 }

---
page6 (2)
Let’s add concurrency...
Every second, read sensor value and broadcast it.
Stop immediately as soon as a message arrives.
Arduino
Céu
 uint32_t lst = millis();
 while (1) {
   if (radioAvail())
     break;
   uint32_t cur = millis();
   if (cur > lst+1000) {
     lst = cur;
     int v = analogRead();
     radioWrite(v);
   }
 }

---
page6 (3)
Let’s add concurrency...
Every second, read sensor value and broadcast it.
Stop immediately as soon as a message arrives.
Arduino
Céu
 uint32_t lst = millis();
 while (1) {
   if (radioAvail())
     break;
   uint32_t cur = millis();
   if (cur > lst+1000) {
     lst = cur;
     int v = analogRead();
     radioWrite(v);
   }
 }
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end

---
page6 (4)
Let’s add concurrency...
Every second, read sensor value and broadcast it.
Stop immediately as soon as a message arrives.
Arduino
Céu
 uint32_t lst = millis();
 while (1) {
   if (radioAvail())
     break;
   uint32_t cur = millis();
   if (cur > lst+1000) {
     lst = cur;
     int v = analogRead();
     radioWrite(v);
   }
 }
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end

---
page6 (5)
Let’s add concurrency...
Every second, read sensor value and broadcast it.
Stop immediately as soon as a message arrives.
Arduino
Céu
 uint32_t lst = millis();
 while (1) {
   if (radioAvail())
     break;
   uint32_t cur = millis();
   if (cur > lst+1000) {
     lst = cur;
     int v = analogRead();
     radioWrite(v);
   }
 }
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end

---
page7 (1)
Standby Considerations
Every second, read sensor value and broadcast it.
Stop immediately as soon as a message arrives.
Arduino
Céu
 uint32_t lst = millis();
 while (1) {
   if (radioAvail())
     break;
   uint32_t cur = millis();
   if (cur > lst+1000) {
     lst = cur;
     int v = analogRead();
     radioWrite(v);
   }
 }
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end

---
page7 (2)
Standby Considerations
Every second, read sensor value and broadcast it.
Stop immediately as soon as a message arrives.
Arduino
Céu
 uint32_t lst = millis();
 while (1) {
   if (radioAvail())
     break;
   uint32_t cur = millis();
   if (cur > lst+1000) {
     lst = cur;
     int v = analogRead();
     radioWrite(v);
   }
 }
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end

---
page7 (3)
Standby Considerations
Every second, read sensor value and broadcast it.
Stop immediately as soon as a message arrives.
Arduino
Céu
 uint32_t lst = millis();
 while (1) {
   if (radioAvail())
     break;
   uint32_t cur = millis();
   if (cur > lst+1000) {
     lst = cur;
     int v = analogRead();
     radioWrite(v);
   }
 }
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end

---
page8 (1)

---
page8 (2)
RocketScream
Low-Power
Arduino

---
page8 (3)
RocketScream
Low-Power
Arduino

---
page8 (4)
 await FOREVER;
RocketScream
Low-Power
Arduino

---
page8 (5)
 await FOREVER;
RocketScream
Low-Power
Arduino

---
page8 (6)
 await FOREVER;
RocketScream
Low-Power
Arduino

---
page8 (7)
 await FOREVER;
 loop do
    emit PIN(13,high);
    await 1s;
    emit PIN(13,low);
    await 1s;
 end
RocketScream
Low-Power
Arduino

---
page8 (8)
 await FOREVER;
 loop do
    emit PIN(13,high);
    await 1s;
    emit PIN(13,low);
    await 1s;
 end
RocketScream
Low-Power
Arduino

---
page8 (9)
 await FOREVER;
 loop do
    emit PIN(13,high);
    await 1s;
    emit PIN(13,low);
    await 1s;
 end
RocketScream
Low-Power
Arduino

---
page8 (10)
 await FOREVER;
 loop do
    emit PIN(13,high);
    await 1s;
    emit PIN(13,low);
    await 1s;
 end
RocketScream
Low-Power
Arduino

---
page8 (11)
 await FOREVER;
 loop do
    emit PIN(13,high);
    await 1s;
    emit PIN(13,low);
    await 1s;
 end
RocketScream
Low-Power
Arduino

---
page8 (12)
 await FOREVER;
 loop do
    emit PIN(13,high);
    await 1s;
    emit PIN(13,low);
    await 1s;
 end
 emit PIN(13, _digitalRead(2));
 loop do
    var bool v = await Pin(2);
    emit PIN(13, v);
 end
RocketScream
Low-Power
Arduino

---
page8 (13)
 await FOREVER;
 loop do
    emit PIN(13,high);
    await 1s;
    emit PIN(13,low);
    await 1s;
 end
 emit PIN(13, _digitalRead(2));
 loop do
    var bool v = await Pin(2);
    emit PIN(13, v);
 end
RocketScream
Low-Power
Arduino

---
page8 (14)
 await FOREVER;
 loop do
    emit PIN(13,high);
    await 1s;
    emit PIN(13,low);
    await 1s;
 end
 emit PIN(13, _digitalRead(2));
 loop do
    var bool v = await Pin(2);
    emit PIN(13, v);
 end
RocketScream
Low-Power
Arduino

---
page8 (15)
 await FOREVER;
 loop do
    emit PIN(13,high);
    await 1s;
    emit PIN(13,low);
    await 1s;
 end
 emit PIN(13, _digitalRead(2));
 loop do
    var bool v = await Pin(2);
    emit PIN(13, v);
 end
RocketScream
Low-Power
Arduino

---
page8 (16)
 await FOREVER;
 loop do
    emit PIN(13,high);
    await 1s;
    emit PIN(13,low);
    await 1s;
 end
 emit PIN(13, _digitalRead(2));
 loop do
    var bool v = await Pin(2);
    emit PIN(13, v);
 end
RocketScream
Low-Power
Arduino

---
page8 (17)
 await FOREVER;
 loop do
    emit PIN(13,high);
    await 1s;
    emit PIN(13,low);
    await 1s;
 end
 emit PIN(13, _digitalRead(2));
 loop do
    var bool v = await Pin(2);
    emit PIN(13, v);
 end
RocketScream
Low-Power
Arduino

---
page8 (18)
 await FOREVER;
 loop do
    emit PIN(13,high);
    await 1s;
    emit PIN(13,low);
    await 1s;
 end
 emit PIN(13, _digitalRead(2));
 loop do
    var bool v = await Pin(2);
    emit PIN(13, v);
 end
 loop do
    await 1s;
    <...>
    await Nrf24l01_TX(...);
    <...>
    await Nrf24l01_RX(...);
    <...>
 end
RocketScream
Low-Power
Arduino

---
page8 (19)
 await FOREVER;
 loop do
    emit PIN(13,high);
    await 1s;
    emit PIN(13,low);
    await 1s;
 end
 emit PIN(13, _digitalRead(2));
 loop do
    var bool v = await Pin(2);
    emit PIN(13, v);
 end
 loop do
    await 1s;
    <...>
    await Nrf24l01_TX(...);
    <...>
    await Nrf24l01_RX(...);
    <...>
 end
RocketScream
Low-Power
Arduino

---
page8 (20)
 await FOREVER;
 loop do
    emit PIN(13,high);
    await 1s;
    emit PIN(13,low);
    await 1s;
 end
 emit PIN(13, _digitalRead(2));
 loop do
    var bool v = await Pin(2);
    emit PIN(13, v);
 end
 loop do
    await 1s;
    <...>
    await Nrf24l01_TX(...);
    <...>
    await Nrf24l01_RX(...);
    <...>
 end
RocketScream
Low-Power
Arduino

---
page8 (21)
 await FOREVER;
 loop do
    emit PIN(13,high);
    await 1s;
    emit PIN(13,low);
    await 1s;
 end
 emit PIN(13, _digitalRead(2));
 loop do
    var bool v = await Pin(2);
    emit PIN(13, v);
 end
 loop do
    await 1s;
    <...>
    await Nrf24l01_TX(...);
    <...>
    await Nrf24l01_RX(...);
    <...>
 end
RocketScream
Low-Power
Arduino

---
page9 (1)
General Approach
(standby, constrained, programming language, transparent)
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end

---
page9 (2)
General Approach
(standby, constrained, programming language, transparent)
- Enforce idle states of execution
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end

---
page9 (3)
General Approach
(standby, constrained, programming language, transparent)
- Enforce idle states of execution
  - Céu enforces a reactive model of execution
- Infer deepest sleeping mode
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end

---
page9 (4)
General Approach
(standby, constrained, programming language, transparent)
- Enforce idle states of execution
  - Céu enforces a reactive model of execution
- Infer deepest sleeping mode
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end

---
page9 (5)
General Approach
(standby, constrained, programming language, transparent)
- Enforce idle states of execution
  - Céu enforces a reactive model of execution
- Infer deepest sleeping mode
  - Céu has a semantics amenable to analysis
- Put device to sleep
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end

---
page9 (6)
General Approach
(standby, constrained, programming language, transparent)
- Enforce idle states of execution
  - Céu enforces a reactive model of execution
- Infer deepest sleeping mode
  - Céu has a semantics amenable to analysis
- Put device to sleep
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end

---
page9 (7)
General Approach
(standby, constrained, programming language, transparent)
- Enforce idle states of execution
  - Céu enforces a reactive model of execution
- Infer deepest sleeping mode
  - Céu has a semantics amenable to analysis
- Put device to sleep
  - Céu has an energy-aware runtime
- Only awake from interrupts
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end

---
page9 (8)
General Approach
(standby, constrained, programming language, transparent)
- Enforce idle states of execution
  - Céu enforces a reactive model of execution
- Infer deepest sleeping mode
  - Céu has a semantics amenable to analysis
- Put device to sleep
  - Céu has an energy-aware runtime
- Only awake from interrupts
  - Céu provides interrupt service routines (ISRs)
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end

---
Transparent Standby for Low-Power,
Resource-Constrained Embedded Systems
A Programming Language-Based Approach
Francisco Sant'Anna
francisco@ime.uerj.br
@_fsantanna
www.ceu-lang.org

---
page12 (1)
Standby Efficiency for IoT

---
page12 (2)
Standby Efficiency for IoT
- 15 billion “traditional” network-connected devices in 2015 (e.g., mobile phones & smart TVs).

---
page12 (3)
Standby Efficiency for IoT
- 15 billion “traditional” network-connected devices in 2015 (e.g., mobile phones & smart TVs).
- 75 billion by 2025 with the IoT (e.g., smart bulbs & fitness wearables). [2016]

---
page12 (4)
Standby Efficiency for IoT
- 15 billion “traditional” network-connected devices in 2015 (e.g., mobile phones & smart TVs).
- 75 billion by 2025 with the IoT (e.g., smart bulbs & fitness wearables). [2016]
- Most energy consumed in standby mode.

---
page12 (5)
Standby Efficiency for IoT
- 15 billion “traditional” network-connected devices in 2015 (e.g., mobile phones & smart TVs).
- 75 billion by 2025 with the IoT (e.g., smart bulbs & fitness wearables). [2016]
- Most energy consumed in standby mode.
- Network standby is one of the six fronts on IEA/G20's Energy Efficiency Action Plan
  - https://www.iea-4e.org/projects/g20

---
page13 (1)
From “Traditional” Internet to “IoT”

---
page13 (2)
From “Traditional” Internet to “IoT”
Today: 15 billion devices

---
page13 (3)
From “Traditional” Internet to “IoT”
Today: 15 billion devices

---
page13 (4)
From “Traditional” Internet to “IoT”
Today: 15 billion devices
Tomorrow: 50 billion devices (2020)

---
page13 (5)
From “Traditional” Internet to “IoT”
Today: 15 billion devices
Tomorrow: 50 billion devices (2020)

---
page13 (6)
From “Traditional” Internet to “IoT”
Today: 15 billion devices
Tomorrow: 50 billion devices (2020)

---
page13 (7)
From “Traditional” Internet to “IoT”
Today: 15 billion devices
Tomorrow: 50 billion devices (2020)

---
page14 (1)
Energy Efficiency for the IoT

---
page14 (2)
Energy Efficiency for the IoT
Challenges: Pollution, Autonomy

---
page14 (3)
Energy Efficiency for the IoT
Challenges: Pollution, Autonomy
Opportunity: Effective “standby”

---
page14 (4)
Energy Efficiency for the IoT
Challenges: Pollution, Autonomy
Opportunity: Effective “standby”
30-50% economy with existing technologies

---
page15 (1)

---
page15 (2)
All IoT devices have software...

---
page15 (3)
All IoT devices have software...

---
page15 (4)
All IoT devices have software...
… which is written in a language

---
page15 (5)
All IoT devices have software...
… which is written in a language

---
page15 (6)
All IoT devices have software...
… which is written in a language
Current languages have not been designed with energy efficiency in mind!

---
page15 (7)
All IoT devices have software...
… which is written in a language
Current languages have not been designed with energy efficiency in mind!

---
page15 (8)
All IoT devices have software...
… which is written in a language
Current languages have not been designed with energy efficiency in mind!

---
page16 (1)
Céu in a Nutshell

---
page16 (2)
Céu in a Nutshell
- Reactive
  - environment in control: events

---
page16 (3)
Céu in a Nutshell
- Reactive
  - environment in control: events
- Imperative
  - sequences, loops, assignments

---
page16 (4)
Céu in a Nutshell
- Reactive
  - environment in control: events
- Imperative
  - sequences, loops, assignments
- Concurrent
  - multiple lines of execution: trails

---
page16 (5)
Céu in a Nutshell
- Reactive
  - environment in control: events
- Imperative
  - sequences, loops, assignments
- Concurrent
  - multiple lines of execution: trails
- Synchronous (based on Esterel)
  - trails synchronize at each external event

---
page16 (6)
Céu in a Nutshell
- Reactive
  - environment in control: events
- Imperative
  - sequences, loops, assignments
- Concurrent
  - multiple lines of execution: trails
- Synchronous (based on Esterel)
  - trails synchronize at each external event
  - trails are always awaiting

---
page16 (7)
Céu in a Nutshell
- Reactive
  - environment in control: events
- Imperative
  - sequences, loops, assignments
- Concurrent
  - multiple lines of execution: trails
- Synchronous (based on Esterel)
  - trails synchronize at each external event
  - trails are always awaiting
- Deterministic
  - always yields the same outcome for a given timeline

---
page17 (1)
Research Non-Goals

---
page17 (2)
Research Non-Goals
- Adaptive Computing
  - QoS (e.g., resolution, frame rate, accuracy)
  - Behavior (e.g., switch UI, disable functionalities)

---
page17 (3)
Research Non-Goals
- Adaptive Computing
  - QoS (e.g., resolution, frame rate, accuracy)
  - Behavior (e.g., switch UI, disable functionalities)
  - Don’t take advantage of standby modes (goal 1)

---
page17 (4)
Research Non-Goals
- Adaptive Computing
  - QoS (e.g., resolution, frame rate, accuracy)
  - Behavior (e.g., switch UI, disable functionalities)
  - Don’t take advantage of standby modes (goal 1)
- Energy-Aware Network Protocols
  - Low-power listening
  - Small periods of duty cycles

---
page17 (5)
Research Non-Goals
- Adaptive Computing
  - QoS (e.g., resolution, frame rate, accuracy)
  - Behavior (e.g., switch UI, disable functionalities)
  - Don’t take advantage of standby modes (goal 1)
- Energy-Aware Network Protocols
  - Low-power listening
  - Small periods of duty cycles
  - Only for networked parts, not automatic (goals 3 & 4)

---
page17 (6)
Research Non-Goals
- Adaptive Computing
  - QoS (e.g., resolution, frame rate, accuracy)
  - Behavior (e.g., switch UI, disable functionalities)
  - Don’t take advantage of standby modes (goal 1)
- Energy-Aware Network Protocols
  - Low-power listening
  - Small periods of duty cycles
  - Only for networked parts, not automatic (goals 3 & 4)
- Complex Hardware Architectures
  - Microprocessors, MMU, OS-based, Smartphones

---
page17 (7)
Research Non-Goals
- Adaptive Computing
  - QoS (e.g., resolution, frame rate, accuracy)
  - Behavior (e.g., switch UI, disable functionalities)
  - Don’t take advantage of standby modes (goal 1)
- Energy-Aware Network Protocols
  - Low-power listening
  - Small periods of duty cycles
  - Only for networked parts, not automatic (goals 3 & 4)
- Complex Hardware Architectures
  - Microprocessors, MMU, OS-based, Smartphones
  - Not constrained embedded platforms (goal 2)

---
page18 (1)
In Practice...

---
page18 (2)
In Practice...
- Hardware infrastructure

---
page18 (3)
In Practice...
- Hardware infrastructure
  - Off-the-shelf Arduinos (ATMega328, Cortex-M0)
- Software infrastructure

---
page18 (4)
In Practice...
- Hardware infrastructure
  - Off-the-shelf Arduinos (ATMega328, Cortex-M0)
- Software infrastructure
  - Implement an energy-aware runtime for Céu

---
page18 (5)
In Practice...
- Hardware infrastructure
  - Off-the-shelf Arduinos (ATMega328, Cortex-M0)
- Software infrastructure
  - Implement an energy-aware runtime for Céu
  - Rewrite device drivers in Céu (timers, ADC, Radio)
- Applications

---
page18 (6)
In Practice...
- Hardware infrastructure
  - Off-the-shelf Arduinos (ATMega328, Cortex-M0)
- Software infrastructure
  - Implement an energy-aware runtime for Céu
  - Rewrite device drivers in Céu (timers, ADC, Radio)
- Applications
  - Rewrite existing IoT applications in Céu

---
page18 (7)
In Practice...
- Hardware infrastructure
  - Off-the-shelf Arduinos (ATMega328, Cortex-M0)
- Software infrastructure
  - Implement an energy-aware runtime for Céu
  - Rewrite device drivers in Céu (timers, ADC, Radio)
- Applications
  - Rewrite existing IoT applications in Céu
    - Time to rewrite, Coding “aesthetics”, Energy consumption

---
page18 (8)
In Practice...
- Hardware infrastructure
  - Off-the-shelf Arduinos (ATMega328, Cortex-M0)
- Software infrastructure
  - Implement an energy-aware runtime for Céu
  - Rewrite device drivers in Céu (timers, ADC, Radio)
- Applications
  - Rewrite existing IoT applications in Céu
    - Time to rewrite, Coding “aesthetics”, Energy consumption

---
page19 (1)
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end

---
page19 (2)
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end

---
page19 (3)
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end
 code AnalogRead (void) -> int do
   PM_SET(PM_ADC, 1);
   do finalize with
     PM_SET(PM_ADC, 0);
   end
   emit ADC_REQUEST;
   int value = await ADC_DONE;
   escape value;
 end

---
page19 (4)
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end
 code AnalogRead (void) -> int do
   PM_SET(PM_ADC, 1);
   do finalize with
     PM_SET(PM_ADC, 0);
   end
   emit ADC_REQUEST;
   int value = await ADC_DONE;
   escape value;
 end

---
page19 (5)
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end
 code AnalogRead (void) -> int do
   PM_SET(PM_ADC, 1);
   do finalize with
     PM_SET(PM_ADC, 0);
   end
   emit ADC_REQUEST;
   int value = await ADC_DONE;
   escape value;
 end

---
page19 (6)
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end
 code AnalogRead (void) -> int do
   PM_SET(PM_ADC, 1);
   do finalize with
     PM_SET(PM_ADC, 0);
   end
   emit ADC_REQUEST;
   int value = await ADC_DONE;
   escape value;
 end

---
page19 (7)
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end
 code AnalogRead (void) -> int do
   PM_SET(PM_ADC, 1);
   do finalize with
     PM_SET(PM_ADC, 0);
   end
   emit ADC_REQUEST;
   int value = await ADC_DONE;
   escape value;
 end

---
page19 (8)
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end
 code AnalogRead (void) -> int do
   PM_SET(PM_ADC, 1);
   do finalize with
     PM_SET(PM_ADC, 0);
   end
   emit ADC_REQUEST;
   int value = await ADC_DONE;
   escape value;
 end

---
page19 (9)
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end
 output void ADC_REQUEST do
    ADMUX = 0x40|(A0&0x07);
    bitSet(ADCSRA, ADIE);
    bitSet(ADCSRA, ADSC);
 end
 code AnalogRead (void) -> int do
   PM_SET(PM_ADC, 1);
   do finalize with
     PM_SET(PM_ADC, 0);
   end
   emit ADC_REQUEST;
   int value = await ADC_DONE;
   escape value;
 end

---
page19 (10)
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end
 output void ADC_REQUEST do
    ADMUX = 0x40|(A0&0x07);
    bitSet(ADCSRA, ADIE);
    bitSet(ADCSRA, ADSC);
 end
 code AnalogRead (void) -> int do
   PM_SET(PM_ADC, 1);
   do finalize with
     PM_SET(PM_ADC, 0);
   end
   emit ADC_REQUEST;
   int value = await ADC_DONE;
   escape value;
 end

---
page19 (11)
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end
 output void ADC_REQUEST do
    ADMUX = 0x40|(A0&0x07);
    bitSet(ADCSRA, ADIE);
    bitSet(ADCSRA, ADSC);
 end
 code AnalogRead (void) -> int do
   PM_SET(PM_ADC, 1);
   do finalize with
     PM_SET(PM_ADC, 0);
   end
   emit ADC_REQUEST;
   int value = await ADC_DONE;
   escape value;
 end

---
page19 (12)
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end
 output void ADC_REQUEST do
    ADMUX = 0x40|(A0&0x07);
    bitSet(ADCSRA, ADIE);
    bitSet(ADCSRA, ADSC);
 end
 async/isr ADC_vect_num do
   bitClear(ADCSRA, ADIE);
   emit ADC_DONE(ADC);
 end
 code AnalogRead (void) -> int do
   PM_SET(PM_ADC, 1);
   do finalize with
     PM_SET(PM_ADC, 0);
   end
   emit ADC_REQUEST;
   int value = await ADC_DONE;
   escape value;
 end

---
page19 (13)
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end
 output void ADC_REQUEST do
    ADMUX = 0x40|(A0&0x07);
    bitSet(ADCSRA, ADIE);
    bitSet(ADCSRA, ADSC);
 end
 async/isr ADC_vect_num do
   bitClear(ADCSRA, ADIE);
   emit ADC_DONE(ADC);
 end
 code AnalogRead (void) -> int do
   PM_SET(PM_ADC, 1);
   do finalize with
     PM_SET(PM_ADC, 0);
   end
   emit ADC_REQUEST;
   int value = await ADC_DONE;
   escape value;
 end

---
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end
 output void ADC_REQUEST do
    ADMUX = 0x40|(A0&0x07);
    bitSet(ADCSRA, ADIE);
    bitSet(ADCSRA, ADSC);
 end
 input ADC_vect_num do
   bitClear(ADCSRA, ADIE);
   emit ADC_DONE(ADC);
 end
 void pm_sleep (void) {
   if (PM_GET(PM_TIMER1)) {
       sleep_1(<...>)
     } else if (PM_GET(PM_ADC)) {
       sleep_2(<...>);
     } else {
       sleep_3(<...>);
     }
   }
 }
 code AnalogRead (void) -> int do
   PM_SET(PM_ADC, 1);
   do finalize with
     PM_SET(PM_ADC, 0);
   end
   emit ADC_REQUEST;
   int value = await ADC_DONE;
   escape value;
 end

---
 par/or do
   await RadioAvail();
 with
   loop do
     await 1s;
     int v = await AnalogRead();
     await RadioWrite(v);
   end
 end
 output void ADC_REQUEST do
    ADMUX = 0x40|(A0&0x07);
    bitSet(ADCSRA, ADIE);
    bitSet(ADCSRA, ADSC);
 end
 input ADC_vect_num do
   bitClear(ADCSRA, ADIE);
   emit ADC_DONE(ADC);
 end
 void pm_sleep (void) {
   if (PM_GET(PM_TIMER1)) {
       sleep_1(<...>)
     } else if (PM_GET(PM_ADC)) {
       sleep_2(<...>);
     } else {
       sleep_3(<...>);
     }
   }
 }
 code AnalogRead (void) -> int do
   PM_SET(PM_ADC, 1);
   do finalize with
     PM_SET(PM_ADC, 0);
   end
   emit ADC_REQUEST;
   int value = await ADC_DONE;
   escape value;
 end

---
page22 (1)
Related Publications

---
page22 (2)
Related Publications
- SenSys’13, ACM Embedded Networked Sensor Systems
  - Safe System-level Concurrency on Resource-Constrained Nodes

---
page22 (3)
Related Publications
- SenSys’13, ACM Embedded Networked Sensor Systems
  - Safe System-level Concurrency on Resource-Constrained Nodes
- TECS’17, ACM Transactions on Embedded Computing Systems
  - The Design and Implementation of the Synchronous Language Céu

---
page22 (4)
Related Publications
- SenSys’13, ACM Embedded Networked Sensor Systems
  - Safe System-level Concurrency on Resource-Constrained Nodes
- TECS’17, ACM Transactions on Embedded Computing Systems
  - The Design and Implementation of the Synchronous Language Céu
- LCTES’18, ACM Conference on Languages, Compilers, and Tools for Embedded Systems
  - A Memory-Bounded, Deterministic and Terminating Semantics
    for the Synchronous Programming Language Céu

---
page22 (5)
Related Publications
- SenSys’13, ACM Embedded Networked Sensor Systems
  - Safe System-level Concurrency on Resource-Constrained Nodes
- TECS’17, ACM Transactions on Embedded Computing Systems
  - The Design and Implementation of the Synchronous Language Céu
- LCTES’18, ACM Conference on Languages, Compilers, and Tools for Embedded Systems
  - A Memory-Bounded, Deterministic and Terminating Semantics
    for the Synchronous Programming Language Céu
- LCTES’18, ACM Conference on Languages, Compilers, and Tools for Embedded Systems
  - WIP: Transparent Standby for Low-Power, Resource-Constrained
    Embedded Systems

---
page22 (6)
Related Publications
- SenSys’13, ACM Embedded Networked Sensor Systems
  - Safe System-level Concurrency on Resource-Constrained Nodes
- TECS’17, ACM Transactions on Embedded Computing Systems
  - The Design and Implementation of the Synchronous Language Céu
- LCTES’18, ACM Conference on Languages, Compilers, and Tools for Embedded Systems
  - A Memory-Bounded, Deterministic and Terminating Semantics
    for the Synchronous Programming Language Céu
- LCTES’18, ACM Conference on Languages, Compilers, and Tools for Embedded Systems
  - WIP: Transparent Standby for Low-Power, Resource-Constrained
    Embedded Systems

---
page23 (1)
Cooperation Opportunities
- Hardware infrastructure
  - Off-the-shelf Arduinos (ATMega328, Cortex-M0)
- Software infrastructure
  - Implement an energy-aware runtime for Céu
  - Rewrite device drivers in Céu (timers, ADC, Radio)
- Applications
  - Rewrite existing IoT applications in Céu
    - Time to rewrite
    - Coding “aesthetics”
    - Energy consumption

---
page23 (2)
Cooperation Opportunities
- Hardware infrastructure
  - Off-the-shelf Arduinos (ATMega328, Cortex-M0)
- Software infrastructure
  - Implement an energy-aware runtime for Céu
  - Rewrite device drivers in Céu (timers, ADC, Radio)
- Applications
  - Rewrite existing IoT applications in Céu
    - Time to rewrite
    - Coding “aesthetics”
    - Energy consumption